SUPPLIER CERTIFICATION	Today's Date: 06/09/2025

Supplier's Name and Address: Purchaser’s Name and Address:
      Veratex, Inc.	Hexcel Composites Ltd, ‘M’ Stores
      336 East 56th Street Grnd Floor Duxford Cambridge
      New York, NY 10022 USA CB2 4QD, United Kingdom
      Phone: 212 683 9300 Fax: 212 889 5573 Phone: 01223838244 Fax: 01223838723

Date of Manufacture: 06/07/2025 Hexcel RMS and Issue: 8251 ISSUE C
Material Description: Style V10401 100% Polyester Tricot Knit Fabric
Expiry Date: 12/07/2026 Batch Number: 20307/5842730 P.O. Number: 10PO0112004

Batch Number 20307/58427300 Specification:
- Structure:	Tricot Knit
- Chemistry:	PET (Polyester)
- Fabric Width:	1305 mm
- I.D. Cores:	7.62cm (3 Inches)263
- Weight:	30 gsm
- Filaments:	20 Denier Monofilaments

Additional Requirements:

- Each roll is to be individually packaged to prevent contamination before finishing
- Maximum roll length 700 meters
- All joints must be flagged with a minimum of 120 m between joints
- The maximum pallet height shall be 1 meter

Packaging Requirements:

- Packaging shall be adequate to prevent loss, damage or deterioration in transit and for up to one year of the product in storage
- An advice note giving details of purchase order number, item description, item number, quantity and RMS number and issue shall accompany each delivery.
- The advice note shall bear the individual piece numbers and roll lengths.
- Containers shall be marked with highly visible labels and marked as required for 3.3.2
_______________________________________________________________________________
Certificate of Conformity

This is to certify that the aforementioned fabric conforms with the PURCHASE REQUIREMENTS

of _8251, Issue C.
RMS

Signature:__________________________________ Date:__________________
 Claude Simon
______________________________________________________________________________________

Certificate of Analysis

This is to certify that the lot covered by this certification has been analyzed and conforms to the specifications set forth in section 3.1 of RMS_8251, Issue C.

Signature:__________________________________ Dated:____________________
Claude Simon